# INAV/SPEEDYBEEF405WING 8.0.1 Mar 28 2025 / 09:52:26 (ae47bcba)
# GCC-13.2.1 20231009

# Timer overrides
timer_output_mode 2 SERVOS
timer_output_mode 7 MOTORS

# Outputs [servo]
servo 1 1000 2000 1500 -100
servo 2 1000 2000 1500 -100

# features
feature GPS
feature PWM_OUTPUT_ENABLE
feature FW_AUTOTRIM

# blackbox
blackbox -NAV_ACC
blackbox NAV_POS
blackbox NAV_PID
blackbox MAG
blackbox ACC
blackbox ATTI
blackbox RC_DATA
blackbox RC_COMMAND
blackbox MOTORS
blackbox -GYRO_RAW
blackbox -PEAKS_R
blackbox -PEAKS_P
blackbox -PEAKS_Y
blackbox SERVOS

# Receiver: Channel map
map TAER

# Ports
serial 2 2 115200 57600 0 115200
serial 4 33554432 115200 115200 0 115200

# Modes [aux]
aux 0 0 0 1700 2100
aux 1 1 3 900 1300
aux 2 11 2 900 1300
aux 3 10 2 1700 2100
aux 4 62 3 900 1700
aux 5 63 3 1300 1700

# Mission Control Waypoints [wp]
#wp 0 invalid

# OSD [osd_layout]
osd_layout 0 0 35 2 H
osd_layout 0 1 12 8 H
osd_layout 0 7 23 14 V
osd_layout 0 9 35 3 V
osd_layout 0 11 33 13 V
osd_layout 0 12 11 14 V
osd_layout 0 13 12 2 V
osd_layout 0 14 35 1 V
osd_layout 0 15 11 1 V
osd_layout 0 20 29 16 V
osd_layout 0 21 11 16 V
osd_layout 0 22 24 2 V
osd_layout 0 23 21 3 V
osd_layout 0 28 33 14 V
osd_layout 0 30 11 15 V
osd_layout 0 31 35 2 V
osd_layout 0 32 11 13 V
osd_layout 0 34 20 1 V
osd_layout 0 97 20 16 H

# master
set gyro_main_lpf_hz = 80
set dynamic_gyro_notch_q = 250
set dynamic_gyro_notch_mode = 3D
set gyro_zero_x = -5
set gyro_zero_y = -2
set gyro_zero_z = -1
set ins_gravity_cmss = 981.659
set gyro_adaptive_filter_min_hz = 20
set acc_hardware = ICM42605
set acczero_x = -2
set acczero_y = -3
set acczero_z = 14
set accgain_x = 4095
set accgain_y = 4100
set accgain_z = 4098
set align_mag = CW270FLIP
set mag_hardware = LIS3MDL
set magzero_x = -543
set magzero_y = -265
set magzero_z = -657
set maggain_x = 735
set maggain_y = 744
set maggain_z = 652
set align_mag_pitch = -1800
set align_mag_yaw = 900
set baro_hardware = SPL06
set blackbox_rate_denom = 2
set motor_pwm_protocol = STANDARD
set align_board_roll = -2
set align_board_pitch = 4
set servo_pwm_rate = 160
set servo_lpf_hz = 30
set small_angle = 180
set applied_defaults = 3
set gps_ublox_use_galileo = ON
set gps_ublox_use_beidou = ON
set gps_ublox_use_glonass = ON
set airmode_type = STICK_CENTER_ONCE
set nav_disarm_on_landing = OFF
set nav_wp_radius = 800
set nav_wp_max_safe_distance = 500
set nav_rth_allow_landing = FS_ONLY
set nav_rth_altitude = 5000
set nav_fw_control_smoothness = 2
set nav_fw_launch_motor_delay = 100
set nav_fw_launch_max_altitude = 5000
set nav_fw_launch_climb_angle = 25
set osd_video_system = HDZERO
set osd_units = IMPERIAL
set i2c_speed = 800KHZ
set vtx_band = 5
set vtx_channel = 8

# control_profile
control_profile 1

set fw_p_pitch = 15
set fw_i_pitch = 5
set fw_d_pitch = 5
set fw_ff_pitch = 80
set fw_p_roll = 15
set fw_i_roll = 3
set fw_d_roll = 7
set fw_p_yaw = 50
set fw_i_yaw = 0
set fw_d_yaw = 20
set fw_ff_yaw = 255
set dterm_lpf_hz = 10
set dterm_lpf_type = PT3
set fw_turn_assist_pitch_gain = 0.400
set nav_fw_pos_z_p = 25
set nav_fw_pos_z_d = 8
set nav_fw_pos_xy_p = 55
set mc_iterm_relax = RPY
set d_boost_min = 1.000
set d_boost_max = 1.000
set d_boost_gyro_delta_lpf_hz = 60
set antigravity_gain = 2.000
set antigravity_accelerator = 5.000
set fw_level_pitch_trim = 5.000
set smith_predictor_delay = 1.500
set tpa_rate = 20
set tpa_breakpoint = 1200
set tpa_on_yaw = ON
set rc_expo = 30
set rc_yaw_expo = 30
set roll_rate = 18
set pitch_rate = 9
set yaw_rate = 3

# control_profile
control_profile 2

set mc_d_pitch = 0
set mc_d_roll = 0
set fw_p_pitch = 0
set fw_i_pitch = 5
set fw_ff_pitch = 80
set fw_p_roll = 15
set fw_i_roll = 3
set fw_p_yaw = 50
set fw_i_yaw = 0
set fw_d_yaw = 20
set fw_ff_yaw = 255
set fw_d_level = 0
set dterm_lpf_hz = 60
set dterm_lpf_type = PT3
set fw_turn_assist_pitch_gain = 0.400
set nav_fw_pos_z_p = 25
set nav_fw_pos_z_d = 8
set nav_fw_pos_xy_p = 55
set mc_iterm_relax = RPY
set d_boost_min = 0.800
set d_boost_max = 1.200
set d_boost_gyro_delta_lpf_hz = 60
set antigravity_gain = 2.000
set antigravity_accelerator = 5.000
set fw_level_pitch_trim = 5.000
set smith_predictor_delay = 1.500
set tpa_rate = 20
set tpa_breakpoint = 1200
set tpa_on_yaw = ON
set rc_expo = 30
set rc_yaw_expo = 30
set roll_rate = 18
set pitch_rate = 18
set yaw_rate = 9

# control_profile
control_profile 3

set fw_p_pitch = 15
set fw_i_pitch = 5
set fw_d_pitch = 5
set fw_ff_pitch = 80
set fw_p_roll = 15
set fw_i_roll = 3
set fw_d_roll = 7
set fw_p_yaw = 50
set fw_i_yaw = 0
set fw_d_yaw = 20
set fw_ff_yaw = 255
set dterm_lpf_hz = 10
set fw_turn_assist_pitch_gain = 0.400
set nav_fw_pos_z_p = 25
set nav_fw_pos_z_d = 8
set nav_fw_pos_xy_p = 55
set d_boost_min = 1.000
set d_boost_max = 1.000
set rc_expo = 30
set rc_yaw_expo = 30
set roll_rate = 18
set pitch_rate = 9
set yaw_rate = 3

# mixer_profile
mixer_profile 1

set platform_type = AIRPLANE
set has_flaps = ON
set model_preview_type = 26
set mixer_pid_profile_linking = ON

# Mixer: motor mixer

mmix reset

mmix 0 1.000 0.000 0.000 1.000
mmix 1 1.000 0.000 0.000 -1.000
mmix 2 1.000 0.000 0.000 0.000

# Mixer: servo mixer
smix reset

smix 0 1 1 100 0 -1
smix 1 2 0 100 0 -1
smix 2 3 29 87 0 -1
smix 3 4 29 -85 0 -1

# mixer_profile
mixer_profile 2

set platform_type = TRICOPTER
set model_preview_type = 1
set motorstop_on_low = OFF
set mixer_pid_profile_linking = ON

# Mixer: motor mixer

mmix reset

mmix 0 1.000 1.000 -0.667 0.000
mmix 1 1.000 -1.000 -0.667 0.000
mmix 2 1.000 0.000 1.330 0.000

# Mixer: servo mixer
smix reset

smix 0 3 2 -90 0 -1
smix 1 4 2 -90 0 -1
smix 2 3 29 -87 0 -1
smix 3 4 29 85 0 -1
smix 4 2 0 50 0 -1
smix 5 1 1 50 0 -1
smix 6 3 38 60 0 -1
smix 7 4 38 -60 0 -1

# battery_profile
battery_profile 1

set vbat_cell_detect_voltage = 435
set vbat_min_cell_voltage = 340
set vbat_warning_cell_voltage = 360
set throttle_idle = 5.000

# battery_profile
battery_profile 2

set throttle_idle = 5.000

# battery_profile
battery_profile 3

set throttle_idle = 5.000

# restore original profile selection
control_profile 2
mixer_profile 2
battery_profile 1